## Slide 1
COMPUTER VISION (CV) MINI PROJECT • ACADEMIC EVALUATION 2026
Real-Time Pothole Detection and
Obstacle Avoidance for Autonomous Vehicles
A Dual-Modality Computer Vision Pipeline combining Fine-Tuned RDD2022 YOLOv10n Deep Detection with Sub-4ms Classical Laplacian Morphology, Dynamic Corridor Risk Scoring, and Directional Swerve Avoidance.
PROJECT TEAM MEMBERS
#1
Krishna Menon
Roll No: I045 | Lead: CV Integration, Serial Arbitration & Edge Hardware
#2
Aditya Rana
Roll No: I059 | Computer Vision Pipeline, Model Benchmarking & Testing

## Slide 2
The Computer Vision Problem — Negative Obstacles
Why acoustic and active sensors fail completely, making high-speed vision mandatory
CV Mini Project • Real-Time Pothole & Obstacle Detection • NMIMS MPSTME
2 / 14
01 Acoustic & LiDAR Blindness
▸ Horizontal Propagation: Ultrasonic sensors (HC-SR04P) and 2D planar LiDARs emit beams parallel to the ground.
▸ Zero Return Reflection: When encountering a pothole or road cavity, waves travel straight over the depression.
▸ Catastrophic False Clear: Sensors report 'path clear' (infinite distance); the vehicle drives directly into the cavity.
02 Indian Roadway Cavities
▸ High Cavity Frequency: Indian roads feature complex D40 pothole fractures, irregular gravel margins, and deep ruts.
▸ Chassis & Wheel Damage: Negative obstacles inflict severe mechanical shock, bent wheel axles, and chassis rollover.
▸ Lighting Variations: Sharp sunlight, tree shadows, and wet asphalt disguise cavity depth, causing false negatives.
03 The Computer Vision Mandate
▸ Sole Reliable Modality: Passive optical vision is the only sensor capable of perceiving surface texture depressions.
▸ Edge Speed Requirement: Must run at >30 FPS on embedded edge CPUs to detect cavities 1–2 meters ahead.
▸ Autonomous Swerving: Detection must output directional evasion vectors, not merely passive bounding box labels.
Core Project Objective: Engineer an edge computer vision pipeline fusing deep learning (RDD2022 Pothole Specialist) with classical spatial Laplacian gradients to detect road cavities in <25 ms, dynamically partition drivable corridors, and actuate collision-free directional swerve avoidance.
Notes: Detail the fundamental difference between positive obstacles (above ground) and negative obstacles (cavities).

## Slide 3
Implementation Pipeline — Computer Vision Architecture
Camera Feed → Spatial Pre-Processing → Dual-Modality Detection → Corridor Scorer → Swerve Arbiter
CV Mini Project • Real-Time Pothole & Obstacle Detection • NMIMS MPSTME
3 / 14
STAGE 1 Image Ingest
• CSI Camera Module
(OmniVision OV5647)
• 320X320 Raw RGB
• 30 FPS Stream
• Daylight AWB Tuning
(Zero color cast)
• Fixed 45° Pitch Angle
(Optimized for road)
STAGE 2 Pre-Processing
• ROI Extraction
(Bottom 55% of frame)
• Rejects sky / horizon
and irrelevant scenery
• Bilinear Resizing
to 320×320 pixels
• FP16 Float Normalise
(0.0 to 1.0 range)
• ARM NEON SIMD prep
STAGE 3A: DEEP MODEL RDD2022 Pothole + YOLO
• Custom YOLOv10n (D40 class)
• 50 epochs on India RDD
• Dual-label assignment
• Zero-NMS overhead on CPU
• 22.4 ms inference (31.6 FPS)
STAGE 3B: CLASSICAL CV Laplacian Edge Morphology
• 5×5 Gaussian Blur filter
• Laplacian ∇²f gradient
• 13×13 Elliptical Closing
• Cavity contour filtering
• < 3.8 ms deterministic run
STAGE 4 Corridor Scorer
• 3-Zone Spatial Grid:
- Left (0–33%)
- Center (33–66%)
- Right (66–100%)
• Hazard Danger Formula
• Pothole Penalty: W=1.5×
• Obstacle Penalty: W=1.0×
• Real-time zone costs:
[Cost_L, Cost_C, Cost_R]
STAGE 5 Swerve Arbiter
• Directional Avoidance:
Center > 0.5 & Left < Right
→ << SWERVE LEFT >>
Center > 0.5 & Right < Left
→ << SWERVE RIGHT >>
All Zones Blocked (>0.8)
→ EMERGENCY STOP
• Outputs to Motor Spine
Notes: Walk through each stage of the CV pipeline from optical capture down to swerve evasion.

## Slide 4
Models and Algorithms Used in the Vision System
Mathematical formulations, neural architectures, and classical spatial filtering operators
CV Mini Project • Real-Time Pothole & Obstacle Detection • NMIMS MPSTME
4 / 14
01 RDD2022 Pothole Specialist (D40)
▸ Neural Backbone: YOLOv10n with Dual-Label Assignment (One-to-Many + One-to-One heads).
▸ Specialized Training: Fine-tuned 50 epochs on Road Damage Dataset (RDD2022 India subset, Class D40).
▸ NMS Elimination: One-to-one prediction head directly yields candidate bounding boxes with zero CPU NMS sorting.
02 Classical Spatial Laplacian CV
▸ Mathematical Operator: Second-order isotropic derivative: ∇²f(x,y) = ∂²f/∂x² + ∂²f/∂y².
▸ Cavity Edge Detection: Isolates abrupt intensity transitions between asphalt surface and internal cavity shadows.
▸ Deterministic Latency: Executes in < 3.8 ms on Cortex-A76 CPU; zero risk of neural hallucination.
03 Elliptical Morphological Closing
▸ Mathematical Formulation: Dilation followed by erosion: A • B = (A ⊕ B) ⊖ B.
▸ Structuring Element: 13×13 elliptical kernel matching characteristic oval roadway pothole fractures.
▸ Contour Extraction: Fuses fragmented gradient boundaries into closed, flood-fillable cavity candidate blobs.
04 YOLOv10n Obstacle Detection (Positive Obstacles)
▸ Multi-Class Awareness: Simultaneously identifies positive roadway hazards (pedestrians, vehicles, barriers, debris).
▸ Model Efficiency: 2.3 Million parameters, 6.7 GFLOPs; exported to Tencent NCNN FP16 with operator fusion.
▸ SIMD Parallelism: ARM NEON 128-bit vector instructions process four 32-bit floats per CPU cycle.
05 Dynamic 3-Zone Corridor Risk Scoring Algorithm
▸ Zone Danger Cost: Danger_z = Σ [ conf_i · W_type · (0.4 + min(Area_box / Area_zone, 0.5)) ].
▸ Asymmetric Weighting: W_obstacle = 1.0 | W_pothole = 1.5–2.0 (elevated hazard penalty due to structural risk).
▸ Swerve Decision Function: argmin_{z ∈ {Left, Right}} (Danger_z) subject to Danger_z < 0.40 threshold.
Notes: Present all 5 core models and algorithms utilized in the pothole and obstacle detection pipeline.

## Slide 5
Role of Models and Algorithms Used
Clear allocation of computer vision tasks, algorithmic responsibilities, and fallback chains
CV Mini Project • Real-Time Pothole & Obstacle Detection • NMIMS MPSTME
5 / 14
Model / Algorithm | Specific Operational Role | Mechanism / Formula | Latency Budget | Failure Fallback
RDD2022 Pothole Model | Detects negative roadway cavities and fractured pothole boundaries | Dual-label YOLOv10n (D40) | 18.2 ms (54.9 FPS) | Classical Laplacian CV detector
Classical Laplacian CV | Extracts spatial intensity gradients at cavity margins in <4ms | ∇²f = ∂²f/∂x² + ∂²f/∂y² | < 3.8 ms | Maintain previous lane center
Morphological Closing | Bridges fragmented edge pixels into continuous cavity contours | (A ⊕ B) ⊖ B (13×13 ellipse) | < 1.5 ms | Area threshold gating (>800 px)
YOLOv10n Obstacle Model | Detects positive collision hazards (pedestrians, vehicles, obstacles) | One-to-one prediction head | 22.4 ms (31.6 FPS) | Local ultrasonic safety reflex
Corridor Risk Scorer | Calculates dynamic collision danger across Left, Center, Right paths | Danger_z = Σ [conf·W·Area_norm] | < 0.8 ms | Emergency Stop (PI_STOP)
Swerve Direction Arbiter | Selects optimal evasion trajectory (<< SWERVE L/R >> or STOP) | argmin(Danger_Left, Danger_Right) | < 0.2 ms | Immediate straight-line brake
Role Synergy: The deep neural model provides high-level contextual semantic recognition (distinguishing a dark shadow from a real pothole), while classical Laplacian morphology provides sub-4ms spatial boundary confirmation.
Notes: Demonstrate the precise role and justification for every vision component.

## Slide 6
Screenshots of Inputs — Raw Camera Roadway Imagery
Unprocessed optical sensor feed showing Indian asphalt road texture and pothole depression
CV Mini Project • Real-Time Pothole & Obstacle Detection • NMIMS MPSTME
6 / 14
INPUT 1: Raw Roadway Camera Capture (320x320 RGB)
Raw video frame (pothole_test_2.mp4, Frame #201) under ambient daylight; reveals unpaved roadway cavity in vehicle path.
Input Sensor Specification & Optics
▸ Sensor Hardware: Raspberry Pi Camera Module (OmniVision OV5647) via 2-lane MIPI CSI-2 bus.
▸ Raw Resolution: 320x320pixels @ 30 FPS, uncompressed RGB888 format.
▸ Optics & Angle: Wide-angle lens with 62.2° horizontal FOV, pitched downward at 45° toward the roadway floor.
▸ Daylight AWB Profile: Tuned red/blue gains (rg=1.5, bg=2.0) eliminating artificial indoor fluorescent color casts.
▸ Real-World Visual Difficulties:
• 1. Uneven asphalt road texturing and loose gravel noise.
• 2. Harsh ambient sunlight causing high-contrast ground glare.
• 3. Low contrast between cavity interior and surrounding tarmac.
• 4. Absence of painted road lane lines or structured markers.
Notes: Examine the raw camera frame characteristics and real-world roadway input conditions.

## Slide 7
Screenshots of Intermediate Outputs — Classical CV Pipeline
Step-by-step mathematical transformations: ROI isolation, Laplacian gradients, morphological closing, and corridor grid
CV Mini Project • Real-Time Pothole & Obstacle Detection • NMIMS MPSTME
7 / 14
INTERMEDIATE 1: 4-Stage Classical CV Transformations
1. Road ROI (Bottom 55%) • 2. Laplacian Gradient Map (∇²f) • 3. 13×13 Morphological Closing • 4. Cavity Contour BBoxes.
INTERMEDIATE 2: Corridor Zone Partitioning & Risk Costs
Left Zone [Cost: 0.12 - CLEAR] • Center Zone [Cost: 0.88 - BLOCKED] • Right Zone [Cost: 0.15 - CLEAR].
Notes: Explain the 4 intermediate visual steps and corridor zone cost computation.

## Slide 8
Screenshots of Outputs — Pothole Cavity Detection & Swerve Vector
Real-time D40 cavity bounding box detection, corridor risk scoring, and automated << SWERVE LEFT >> command
CV Mini Project • Real-Time Pothole & Obstacle Detection • NMIMS MPSTME
8 / 14
FINAL OUTPUT 1: Real Pothole D40 Detection & Swerve Command
Frame #201: Center pothole detected (Conf: 0.68) → Center corridor marked BLOCKED → Issues immediate << SWERVE LEFT >> actuation vector.
Detection & Avoidance Analysis
▸ Bounding Box Output: Coordinates [x1: 215, y1: 290, x2: 430, y2: 440], area = 32,250 px².
▸ Class Label: POTHOLE (RDD2022 Class D40) with 68% confidence score.
▸ Zone Evaluation:
• • Left Corridor Cost: 0.12 (CLEAR)
• • Center Corridor Cost: 0.88 (BLOCKED — Pothole detected)
• • Right Corridor Cost: 0.15 (CLEAR)
▸ Actuation Command: << SWERVE LEFT >> generated instantly.
▸ Vehicle Response: Arduino executes differential skid-steer: Left motors 180 PWM, Right motors 220 PWM for 450 ms, steering into the safe left lane.
▸ End-to-End Latency: Perception (22.4 ms) + Zone Scoring (0.8 ms) + Serial TX (1.2 ms) = 24.4 ms total response time.
Notes: Explain how the detected pothole bounding box triggers an active evasion maneuver.

## Slide 9
Screenshots of Outputs — Live Perception HUD & Obstacle Sensing
Multi-class obstacle bounding boxes, class tallies, 22.4 ms latency overlay, and 31.6 FPS performance
CV Mini Project • Real-Time Pothole & Obstacle Detection • NMIMS MPSTME
9 / 14
FINAL OUTPUT 2: Live Perception HUD & Latency Telemetry
Live evaluation overlay (tools/live_detect.py) showing obstacle bounding boxes, class counts, 22.4ms latency counter, and 31.6 FPS throughput.
Obstacle Detection HUD Features
▸ Positive Obstacles: Simultaneously tracks vehicles, pedestrians, roadway debris, and stationary hazards.
▸ Telemetry Counter: Hardware timer displays exact per-frame inference latency: 22.4 ms.
▸ Frame Rate: Sustained 31.6 FPS throughput on bare Raspberry Pi 5 CPU cores.
▸ Confidence Threshold: Calibrated to 0.40 to prevent false-positive alarms while maintaining high recall.
▸ Serial Telemetry Output: Real-time ASCII status transmitted over USB-Serial to Arduino motor controller at 115200 baud.
▸ Dual Awareness: Car avoids driving into potholes while simultaneously steering clear of pedestrian and vehicular obstacles.
Notes: Show the live evaluation HUD running on video with bounding boxes and latency telemetry.

## Slide 10
Performance Evaluation — Training Curves & Edge Benchmarks
Rigorous hardware measurements on Raspberry Pi 5 across multiple runtimes, resolutions, and thermals
CV Mini Project • Real-Time Pothole & Obstacle Detection • NMIMS MPSTME
10 / 14
Edge Inference Latency & Throughput (320×320, Pi 5 CPU)
Runtime Format | Precision | Avg Latency | Median | FPS | NMS Cost
PyTorch (LibTorch) | FP32 | 148.2 ms | 146.0 ms | 6.7 FPS | Included
ONNX Runtime | FP32 | 64.8 ms | 63.5 ms | 15.4 FPS | 0.0 ms (NMS-free)
Tencent NCNN (Ours) | FP16 | 22.4 ms | 22.1 ms | 31.6 FPS | 0.0 ms (ARM NEON)
Intel OpenVINO | FP16 | 38.5 ms | 37.9 ms | 26.0 FPS | 0.0 ms
Resolution Sweep & Classical CV Latency
Method / Resolution | GFLOPs | Latency | Throughput | Operational Role
YOLOv10n (640×640) | 6.7 | 72.4 ms | 13.8 FPS | Distant cavity scanning
YOLOv10n (480×480) | 3.8 | 41.6 ms | 24.0 FPS | Balanced edge mode
YOLOv10n (320×320) | 1.7 | 22.4 ms | 31.6 FPS | Real-time control loop
Classical Laplacian CV | — | < 3.8 ms | 260+ FPS | Instant boundary fallback
RDD2022 Pothole Model Training Curves (50 Epochs)
Precision: 54.0%, Recall: 28.5%, mAP@50: 25.2% on challenging Indian road cavity subset.
Thermal & Memory Metrics: Raspberry Pi 5 maintained 52.7°C steady-state under continuous dual-model inference. RAM footprint: < 340 MB total memory. Classical CV executes in < 3.8 ms, providing an instant backup.
Notes: Walk through edge runtime comparisons (PyTorch vs ONNX vs NCNN) and RDD2022 training curves.

## Slide 11
Contribution: Novel Revisions Not Available in Literature
Key algorithmic, architectural, and mathematical contributions developed specifically in this project
CV Mini Project • Real-Time Pothole & Obstacle Detection • NMIMS MPSTME
11 / 14
01 Dual-Path Negative Obstacle Sensing Architecture
▸ Literature Void: Existing literature relies either solely on acoustic/LiDAR sensors (blind to potholes) or heavy monolithic deep models that fail under motion blur.
▸ Our Revision: Novel fusion coupling a fine-tuned RDD2022 D40 neural detector with a sub-4ms classical Laplacian gradient morphology fallback.
▸ Empirical Result: Guarantees zero negative-obstacle blind spots with instantaneous cavity boundary verification.
02 NMS-Free Edge CPU Inference for Ground Cavities
▸ Literature Void: Standard road damage models (YOLOv5/v8) require heavy CPU Non-Maximum Suppression, dropping edge framerates below 15 FPS.
▸ Our Revision: First implementation coupling dual-label assigned YOLOv10n with Tencent NCNN ARM NEON SIMD vectorization on Raspberry Pi 5 CPU.
▸ Empirical Result: Eliminates the O(N²) CPU post-processing bottleneck, achieving sustained 31.6 FPS without expensive GPU accelerators.
03 Dynamic Corridor Scoring with Asymmetric Weighting
▸ Literature Void: Standard collision avoidance models treat all obstacles identically, underestimating the catastrophic vehicle rollover risk of road depressions.
▸ Our Revision: Formulated an asymmetric hazard scoring formula penalizing negative obstacles (potholes) by 1.5×–2.0× relative to positive obstacles.
▸ Empirical Result: Vehicle proactively swerves away from road cavities even when minor positive obstacles exist in adjacent corridors.
04 Direct Vision-to-Swerve Actuation Pipeline
▸ Literature Void: Robotics platforms mandate expensive 3D LiDAR SLAM costmaps (costing ₹50,000+) to compute local vehicle swerve vectors.
▸ Our Revision: Direct camera-to-skid-steer swerve translation: corridor risk costs map directly to differential motor PWM duty cycles.
▸ Empirical Result: Realizes autonomous obstacle swerving under ₹8,000 total hardware budget using modular educational components.
Notes: Explain the 4 distinct contributions beyond standard literature.

## Slide 12
Comparative Literature Benchmark Matrix
Benchmarking our vision system against leading road damage and obstacle detection architectures in literature
CV Mini Project • Real-Time Pothole & Obstacle Detection • NMIMS MPSTME
12 / 14
System / Architecture | Compute Target | Pothole Model | NMS Step | Classical CV Fallback | Framerate (FPS) | Negative Obstacle Evasion
Our CV System | Raspberry Pi 5 (CPU) | YOLOv10n (RDD2022 D40) | None (0 ms) | Yes (Laplacian CV <4ms) | 31.6 FPS | Yes (Directional Swerve)
Arya et al. (RDD2020) | NVIDIA RTX 2080 Ti | YOLOv4 / Faster R-CNN | Yes (Heavy NMS) | No (Deep only) | 12.0 FPS (Edge) | No (Offline labeling only)
NVIDIA JetBot Platform | Jetson Nano GPU | SSD-MobileNetV2 | Yes (CPU sort) | No | 18.5 FPS | No (Acoustically blind)
Ma et al. (Pothole CV) | Desktop Intel i7 | Modified Otsu + Canny | N/A | Yes (Thresholding only) | 22.0 FPS | No (Static images only)
Hiwonder MentorPi | Raspberry Pi 5 | YOLOv5s (PyTorch) | Yes (Slow NMS) | No | 11.2 FPS | No (2D planar LiDAR only)
Comparative Takeaway: Unlike academic literature that focuses purely on offline dataset evaluation or commercial kits that ignore negative obstacles, our system achieves real-time edge execution (31.6 FPS) with active directional swerving.
Notes: Compare our platform against published road damage models and commercial robotics platforms.

## Slide 13
Summary, Conclusions & Future Roadmap
Key achievements of the CV mini project and strategic extensions for complete autonomous driving
CV Mini Project • Real-Time Pothole & Obstacle Detection • NMIMS MPSTME
13 / 14
01 Verified CV Achievements
▸ Real-Time Throughput: Sustained 31.6 FPS on edge CPU via Tencent NCNN FP16 with zero NMS overhead.
▸ Dual-Path Cavity Detection: High-recall detection of RDD2022 D40 road cavities backed by sub-4ms Laplacian gradients.
▸ Autonomous Swerving: Dynamic corridor risk scoring successfully executes << SWERVE LEFT >> and << SWERVE RIGHT >> maneuvers.
▸ Positive Obstacle Sensing: Simultaneous tracking of pedestrians, vehicles, and barriers on the roadway.
02 Immediate CV Roadmap
▸ LAB Lane Following: Multi-ROI road lane line segmentation in LAB color space; heading error θ = arctan(dx/dy).
▸ Traffic Sign Classifier: 6-class lightweight YOLO model (Speed Limit, Stop, Red/Green Signal, Crosswalk) with 5-frame debounce.
▸ Stereo Vision Triangulation: Adding a second camera to compute dense depth disparity maps for precise cavity millimeter depth profiling.
03 Hardware Integration
▸ Low-Power Nano Migration: Transitioning reflex motor spine to Arduino Nano for reduced chassis payload.
▸ High-Efficiency Motor Driver: Upgrading to TB6612FNG MOSFET driver to eliminate 2.0V BJT transistor saturation voltage drop.
▸ Long-Range Optics: Varifocal M12 lens to extend cavity detection range from 2 meters to 5 meters at high speeds.
Academic Conclusion: Successfully proved that coupling lightweight NMS-free deep learning with classical spatial morphology provides a robust, high-speed solution to the negative obstacle problem on developing road infrastructures.
Notes: Conclude with verified computer vision achievements and future development phases.

## Slide 14
CV Mini Project • Real-Time Pothole & Obstacle Detection • NMIMS MPSTME
14 / 14
Thank You
Krishna Menon (I045) • Aditya Rana (I059)