## Slide 1
B.TECH CAPSTONE PROJECT • NMIMS MPSTME
Autonomous Follow-Me & Obstacle-Avoidant
Robotic Vehicle
Two-Layer Architecture (Raspberry Pi 5 + Arduino Uno) with NMS-Free YOLOv10n on Tencent NCNN, Pothole Detection and Hard Real-Time Reflex Control
Krishna Menon • Aditya Rana • Parth Surve
Guide: ____________________
📷 SCREENSHOT
Photo of the assembled car
Front 3/4 view, camera visible
Notes: Introduce the team and the one-line pitch: a low-cost two-layer autonomous car that does person following, obstacle avoidance and pothole detection.

## Slide 2
Problem Statement & Research Gaps
Why a single Linux board driving motors directly is not enough
Model-Car Capstone | NMIMS MPSTME
2
01 Timing & Safety
▸ Linux CFS scheduler gives no real-time guarantees
▸ Software PWM jitters under heavy neural inference
▸ Camera → decision → motor loop is too slow for last-moment braking
02 Negative Obstacles
▸ Ultrasonic waves travel horizontally
▸ Potholes / drop-offs give no echo → reads as "path clear"
▸ Indian roads make pothole awareness essential
03 Cost & Access
▸ Commercial AI car kits are imported & costly
▸ Need a modular build from locally available parts
▸ Re-use of college lab assets (Pi 5, Arduino, camera)
Objective: decouple perception (Pi 5) from actuation (Arduino) so that vision can be heavy while braking and motor timing stay deterministic — and add camera-based pothole detection.
Notes: Gap 1: Linux is not real-time; PWM and braking latency suffer under heavy inference. Gap 2: ultrasonic sensors cannot see potholes. Gap 3: commercial kits are expensive in India.

## Slide 3
System Architecture — The Two-Layer Split
Cognitive brain + reflexive spine, connected over USB serial
Model-Car Capstone | NMIMS MPSTME
3
Raspberry Pi 5 (8 GB) — High-Level
Quad Cortex-A76 @ 2.4 GHz
• CSI camera ingest (640×480)
• YOLOv10n on Tencent NCNN
• Pothole engine (RDD2022 YOLOv10n + CV)
• KCF tracker + HSV re-ID
• PID steering & decision arbiter
Arduino Uno R3 — Real-Time
ATmega328P @ 16 MHz
• Hardware Timer0 PWM (D5 / D6)
• 2× HC-SR04P sonar, 2× IR
• 3-tier priority state machine
• Local reflex avoidance (< 20 cm)
• Watchdog failsafe
DRIVE / TURN / PI_STOP
[TELEM] / [ACK]
USB 115200 8N1
Logic Rail (isolated)
USB-C power bank 5.1 V / 5 A → Pi 5
Motor Rail
2S 18650 (7.4 V) → buck 5 V → Arduino / L298N → 4× TT motors
Notes: Pi 5 runs all vision and decision making. Arduino owns PWM, sonar timing and the reflex. If the Pi crashes, the Arduino watchdog stops the motors.

## Slide 4
Perception Model — Why YOLOv10n?
End-to-end detection without Non-Maximum Suppression
Model-Car Capstone | NMIMS MPSTME
4
Traditional YOLO (v5 / v8)
Backbone + Neck
One-to-many head
many overlapping candidate boxes
NMS post-processing
IoU sort & suppress on CPU
Final detections
YOLOv10 (NMS-free)
Backbone + Neck
One-to-one head
one box per object
Final detections
no NMS step
YOLOv10n at a glance
▸ Params: 2.3 M
▸ Compute: 6.7 GFLOPs (640 input)
▸ Trained on: COCO, 80 classes
▸ Classes used: person, bicycle, car, motorcycle, bus, truck
▸ Training trick: dual label assignment (one-to-many + one-to-one)
▸ Inference: one-to-one head only → no NMS
▸ Source: Wang et al., arXiv:2405.14458 (2024)
Notes: Older YOLOs output many overlapping boxes and need NMS on the CPU. YOLOv10 trains with dual label assignment and uses the one-to-one head at inference, so NMS is removed.

## Slide 5
Inference Engine — Why Tencent NCNN on the Pi 5 CPU?
Making a CPU-only board run real-time detection
Model-Car Capstone | NMIMS MPSTME
5
ARM NEON SIMD
128-bit vector instructions on Cortex-A76 process several values per instruction
FP16 weights
Half-precision export halves model size and memory bandwidth
Operator fusion
Conv + BatchNorm + activation merged into a single pass
Light runtime
No Python/PyTorch overhead in the inner loop; pre-allocated buffers
📷 SCREENSHOT
benchmark.py output on Raspberry Pi 5
PyTorch FP32 vs ONNX vs NCNN FP16 vs OpenVINO FP16 — latency / FPS table
Export pipeline:
yolov10n.pt → model.export(format="ncnn", imgsz=320, half=True) → yolov10n_ncnn_model/
Notes: Explain each pillar briefly, then point at the benchmark screenshot comparing PyTorch, ONNX, NCNN and OpenVINO on the Pi 5.

## Slide 6
Complete Software Pipeline
Camera frame → perception → decision → serial command → reflex firmware → motors
Model-Car Capstone | NMIMS MPSTME
6
RASPBERRY PI 5 (Python)
ARDUINO UNO (C++ firmware, 100 Hz loop)
Camera
640×480 @ 30 FPS
Pre-process
resize / ROI crop
YOLOv10n · NCNN
people, vehicles
Pothole engine
RDD2022 YOLOv10n + CV
Zone scorer
Left / Centre / Right
Decision arbiter
PI_STOP
emergency latch
PI_AVOID L/R
directional swerve
Follow-Me
KCF + HSV re-ID → PID
USB-Serial 115200 8N1 — ASCII commands: DRIVE · TURN · REV · STOP · PI_STOP · PI_GO · PI_AVOID ⇅ [TELEM] / [ACK] replies
Tier 1
PI_STOP latch / watchdog
Tier 2
sonar < 20 cm → reverse, turn, resume
Tier 3
execute DRIVE / TURN
L298N driver
PWM D5 / D6, dir D8–D11
4× TT motors
skid-steer
2× HC-SR04P + 2× IR
Notes: Walk left-to-right across the Pi 5 row, down through the serial link, then right-to-left across the Arduino row. Emphasise that sonar feeds the Arduino directly, bypassing Linux.

## Slide 7
Negative Obstacles — Dual-Path Pothole Engine
What ultrasonic sensors cannot see, the camera must
Model-Car Capstone | NMIMS MPSTME
7
Path A — Deep model
▸ Custom YOLOv10n fine-tuned on RDD2022 (India subset, D40 pothole class)
▸ 50 training epochs • weights: best.pt (YOLOv10n)
▸ Validation: Precision 54.0 %, mAP@50 25.2 %
Path B — Classical CV fallback
ROI
bottom 55 %
Gaussian
5×5
Laplacian
edges
Morphology
13×13 ellipse
Contour
filters
Contour filters: 900 px < area < 25 % of ROI, aspect ratio 0.25–5.0
Zone danger score
Danger = conf × W × (0.4 + min(A_box / A_frame, 0.5))
W = 1.0 normal obstacle • W = 1.2–2.0 pothole
📷 SCREENSHOT
Pothole detection output frame
Corridor overlay + swerve decision
📷 SCREENSHOT
Training curves (results.png)
runs_rdd/custom_pothole_model — loss & mAP vs epoch
Notes: Path A is the trained deep model; Path B is a fast classical fallback. Both feed the same zone scorer, with potholes weighted higher than normal obstacles.

## Slide 8
Follow-Me Tracking & Re-Identification
Lock onto one person, keep following, recover after occlusion
Model-Car Capstone | NMIMS MPSTME
8
Target lock
YOLO person box
KCF tracker
fast frame-to-frame
Lost?
occlusion / exit
Re-ID
HSV torso histogram
PID control
steer + distance
Re-identification (tracker.py)
▸ 2-D H×S histogram (30×32 bins) of the upper torso stored on lock
▸ Candidates compared with Bhattacharyya distance
▸ Best match above the similarity threshold becomes the target again
PID visual servoing (pid.py)
▸ u(t) = Kp·e + Ki·Σe·Δt + Kd·Δe/Δt
▸ Steering error = (x_box − x_centre) / frame width
▸ Distance error = h_box / h_frame − 0.30 (target box height)
📷 SCREENSHOT
Follow-me demo frame
Target box + re-ID score + PID output
Notes: KCF keeps the box between YOLO frames. If the target is lost, the car stops, YOLO finds candidates, and the HSV torso histogram picks the right person again.

## Slide 9
Firmware — 3-Tier Priority State Machine
Safety decisions that never wait for Linux
Model-Car Capstone | NMIMS MPSTME
9
TIER 1 — Emergency
▸ PI_STOP: PWM → 0 instantly, latch until PI_GO
▸ Watchdog: no valid packet within WATCHDOG_TIMEOUT_MS → motors off
▸ Movement commands rejected while latched
TIER 2 — Local reflex
▸ Trigger: either sonar < 20 cm
▸ Reverse 400 ms → turn away 500 ms → resume
▸ PI_AVOID hint overrides turn direction; 500 ms cooldown
TIER 3 — Navigation
▸ DRIVE <speed> <ms>, REV, TURN <deg> <speed>, STOP
▸ Hardware Timer0 PWM on D5 / D6 (0–255)
▸ Sent by the Pi 5 decision arbiter
📷 SCREENSHOT
Serial monitor log
e.g. [TELEM] AVOID triggered / [ACK] BLOCKED (PI_STOPPED)
Notes: Tier 1 always wins. Tier 2 reacts to sonar on the Arduino itself. Tier 3 executes the Pi's movement commands. Values below come from protocol.h / the firmware.

## Slide 10
Our Benchmark Results (Raspberry Pi 5)
Fill with numbers measured on the car — cells marked __
Model-Car Capstone | NMIMS MPSTME
10
Runtime comparison (imgsz 320, 100 frames)
Format | Avg latency (ms) | Median (ms) | FPS | Det / frame
PyTorch FP32 | __ | __ | __ | __
ONNX FP32 | __ | __ | __ | __
NCNN FP16 | __ | __ | __ | __
OpenVINO FP16 | __ | __ | __ | __
Resolution sweep (NCNN FP16)
Input size | Avg latency (ms) | FPS | Det / frame
640 × 640 | __ | __ | __
480 × 480 | __ | __ | __
320 × 320 | __ | __ | __
📷 SCREENSHOT
Terminal: benchmark comparison table
python benchmark.py --video dashcam_test.mp4
📷 SCREENSHOT
htop / vcgencmd measure_temp during run
CPU load & temperature under NCNN
Notes: Run benchmark.py on the Pi 5 and copy the numbers here. Keep the screenshot as evidence.

## Slide 11
Comparison with Similar Platforms
Perception stack and obstacle handling (see report §2 for sources)
Model-Car Capstone | NMIMS MPSTME
11
Platform | Primary model | Params | NMS step | Compute | Obstacle sensing | Pothole
Our vehicle | YOLOv10n (NCNN) | 2.3 M | None | Pi 5 CPU | Camera + 2× sonar reflex | Yes
NVIDIA JetBot | SSD-MobileNetV2 / ResNet-18 | 4.3 M / 11.7 M | Yes (SSD) | Jetson Nano GPU | Camera classifier | No
AWS DeepRacer | PPO policy CNN | small | N/A | Intel Atom | Camera / LiDAR (RL) | No
Duckietown DB21 | Classical lane pipeline | — | N/A | Jetson Nano | AprilTags + camera | No
OpenBot | MobileNet-SSD / CNN | ~4 M | Yes | Smartphone | 1× sonar + camera | No
DonkeyCar | Behavioural-cloning CNN | ~1.6 M | N/A | Pi 4B | None (track racing) | No
SunFounder PiCar-X | TFLite demos | — | Yes | Pi 4B | 1× sonar, grayscale | No
Hiwonder MentorPi | YOLOv5s | 7.2 M | Yes | Pi 5 | LiDAR + sonar | No
Verify every row against report §2 before presenting; keep citations on the report slide/handout.
Notes: Values are taken from the comparative benchmarking report, section 2, with citations there.

## Slide 12
Live Demo — YOLOv10n on Any Video
test_yolov10_video.py: HUD with latency, FPS and object counts
Model-Car Capstone | NMIMS MPSTME
12
Commands
▸ python test_yolov10_video.py --video pothole_test_2.mp4
▸ python test_yolov10_video.py --video <any_video.mp4>
▸ python test_yolov10_video.py --webcam 0
▸ add --save demo.mp4 to record
Controls
▸ p pause / resume s screenshot q quit
📷 SCREENSHOT
Demo HUD frame
Bounding boxes + latency / FPS overlay
Notes: Run the script live. Use 'p' to pause on an interesting frame and explain the boxes.

## Slide 13
Roadmap — Next Integrations
Three capabilities, nothing else
Model-Car Capstone | NMIMS MPSTME
13
01 Pothole avoidance
▸ Run RDD2022 YOLOv10n + CV fallback in the live loop
▸ Validate corridor + swerve decisions on real surfaces
▸ Tune POTHOLE_WEIGHT and thresholds
02 Lane following
▸ Multi-ROI lane detector in LAB colour space
▸ Heading error θ = arctan(dx / dy)
▸ Feed θ into the existing PID controller
03 Traffic signs & signals
▸ 6 classes: go, right, park, red, green, crosswalk
▸ 5-frame debounce + upper-ROI gating
▸ Red = stop latch, green = release, crosswalk = slow
Status update: ____________________
Notes: Pothole integration on the live car, lane following, and traffic sign recognition.

## Slide 14
Model-Car Capstone | NMIMS MPSTME
14
Thank You
Questions?
Krishna Menon • Aditya Rana • Parth Surve
Notes: Open the floor for questions.